Exposure Control Plan for Chip Hammering and Jackhammering

Chipping or jackhammering concrete without proper dust controls can generate high levels of silica-containing dust. Breathing in this fine dust can cause a serious lung disease called silicosis, which is characterized by scarring and thickening of the lungs, and can result in death.

|  |  | Protecting workers when chipping or jackhammering concrete |
| --- | --- | --- |

| This document will help employers develop an exposure control plan (ECP) for work involving chipping or jackhammering concrete. An ECP is a requirement of the Occupational Health and Safety Regulation (the Regulation). The ECP sets out a detailed approach to protecting workers from harmful exposure to crystalline silica dust. Employers can use this document as a template, and add specific details regarding safe work practices in their operations. This document covers the points employers need to follow to protect workers from harmful exposure. It is important to follow all the points, or use equally effective measures. Tools and equipment for chipping or jackhammering Many tool manufacturers are designing chippers and jackhammers that come equipped with dust control devices (for example, a dust boot connected to a local exhaust system). Chippers and jackhammers come in both gas-powered and electric models. Only use gas-powered equipment in well-ventilated areas. Vacuums Both dry and wet vacuums may used. These need to be fitted with HEPA filtration to prevent respirable silica from entering the workplace air. Vacuums must be inspected and maintained as per the manufacturer’s instructions. Spare filters should be available at the worksite. Equipment tips Invest in good quality equipment and keep it well maintained. Well-designed and maintained equipment significantly reduces dust and lasts longer between replacement and maintenance. Respirator program Employers whose workers wear respirators are required to develop and implement a respirator protection program. The WorkSafeBC publication Breathe Safer provides guidance for developing this program. Hearing conservation Construction workers are exposed to high levels of noise. Over time, workers exposed to these noise levels will suffer hearing loss. Noise hazard signage must be posted in these areas. Workers must wear appropriate hearing protection in these areas. Additional information The following publications are available from WorkSafeBC.com: Breathe Safer (click Publications) Toolbox Meeting Guides for Hazardous Materials: Silica (click Safety at Work, then in the Quick Links section click Toolbox Meeting Guides, and then click Hazardous Materials) For more information about health and safety, employers and workers can call the WorkSafeBC Prevention Information Line, and ask to speak with an occupational hygiene officer. Call 604 276-3100 in the Lower Mainland or 1 888 621-7233 toll-free in B.C. Useful links HSE leaflets on silica and construction can be downloaded free from the HSE web site at www.hse.gov.uk/pubns. NIOSH publications are available at no charge at www.cdc.gov/niosh (search silica and construction). |  | Company information [Name] [Address] [Contact information — names and phone numbers] Worksite information [Project name] [Address] Health hazards from silica exposure Long-term exposure to airborne crystalline silica (for example, quartz) can cause a disabling, sometimes fatal lung disease called silicosis. Exposure to crystalline silica has been linked to lung cancer. When the dust is inhaled deep into the lungs, microscopic particles of silica can cause scar tissue to form in the lung tissue, which restricts the lungs’ ability to extract oxygen from the air. This damage is permanent, but symptoms of the disease may not appear for many years. The disease initially causes fatigue and shortness of breath. If exposure continues, it can lead to chest pain, heart problems (difficulty breathing can strain the heart), and respiratory failure. Exposure to crystalline silica has also been linked to other diseases, including bronchitis and tuberculosis. Purpose and responsibilities [Company name] has a duty to protect our workers from silica exposure during chipping and jackhammering concrete. Studies show that these operations generate airborne silica levels well in excess of safe levels. Effective controls are available to protect workers from harmful exposure. A combination of control measures will be required to achieve this objective. We commit to being diligent in our efforts to select the most effective control technologies available, and to ensure that the best practices, as described in this exposure control plan (ECP), are followed at our worksites. The work procedures we establish will protect not only our workers but also any other workers on-site who are not involved in these operations. The employer is responsible for the following: Ensure that the materials (for example, tools, equipment, and personal protective equipment [PPE]) and other resources (for example, worker training) required to fully implement and maintain this ECP are readily available. Ensure that supervisors and workers are educated in the hazards of silica exposure and trained to work safely with silica. Maintain written records of training (for example, proper use of respirators), fit-test results, crew talks, and inspections (for equipment, PPE, and work methods and practices). Conduct an annual review (or more often if conditions change) of the effectiveness of the ECP. This includes a review of available dust control technologies to ensure these are selected and used when practical. Coordinate work with the prime contractor and other employers to ensure a safe work environment. Supervisors are responsible for the following: Provide adequate instruction to workers on the hazards of silica associated with chipping and jackhammering concrete. Select and implement the appropriate control measures. Ensure that workers using respirators have been properly trained and fit-tested, and that the results are recorded. Ensure that work is conducted in a manner that minimizes and adequately controls the risk to workers and others. This includes ensuring that workers use appropriate engineering controls and wear the necessary PPE. Workers are responsible for the following: Use the assigned protective equipment in an effective and safe manner. Follow established work procedures as directed by the supervisor. Report any unsafe conditions or acts to the supervisor. Report to the employer any exposure incidents or any signs or symptoms of silica illness. Risk identification and assessment Concrete can contain a high percentage of silica. Chipping and jackhammering concrete without the use of proper dust controls and PPE can expose workers to levels of airborne respirable crystalline silica that are above the exposure limit listed in the Regulation. Work locations where workers or other persons are exposed to the hazards of silica will be identified with signs, placards, or barrier tape. Exposure limit The occupational exposure limit (OEL) for respirable crystalline silica (including quartz) is 0.025 milligrams per cubic metre (mg/m3). Because crystalline silica is linked to lung cancer, workplace exposures must be reduced to levels that are As Low As Reasonably Achievable (ALARA) below the OEL. Silica dust control The Regulation requires employers to select silica dust controls based on the following hierarchy: Engineering (for example, local exhaust ventilation or water attachments) Administrative controls (for example, chipping when other workers are not in the area) Personal protective equipment (for example, respirators and disposable coveralls) Use of respirators as a primary control is not acceptable when other methods are available and practical. Respirators will be used in conjunction with other controls such as local exhaust ventilation (LEV) or water attachments to reduce worker exposure to silica, unless air monitoring information suggests otherwise. LEV and water are the preferred engineering methods, and will be used when practicable. A HEPA vacuum will be used for cleanup and decontamination. Acceptable control methods for chipping or jackhammering concrete The work methods in the following table are acceptable, provided that the respirator selection, dust suppression, and other controls are adhered to. The following control options will be used to eliminate or reduce the risk to workers from the hazards of silica dust exposure, unless air monitoring information suggests otherwise: Work activity Dust suppression Other controls Respirator type Chipping small areas of walls or ceilings LEV (could include a negative air unit or HEPA vacuum positioned near the working surface) Barriers (for example, a tape barrier) to restrict access to the work area Half-face respirator with 100 series (N, P, or R) filters Continuous water spray (could include a portable airless sprayer, air mister, or hose sprayer) Barriers (for example, a tape barrier) to restrict access to the work area Half-face respirator with 100 series (N, P, or R) filters Chipping large areas of walls or ceilings LEV (could include a negative air unit or HEPA vacuum positioned near the working surface) Barriers (for example, a tape barrier) to restrict access to the work area Full-face respirator with 100 series (P or R) filters Continuous water spray (could include a portable airless sprayer, air mister, or hose sprayer) Barriers (for example, a tape barrier) to restrict access to the work area Full-face respirator with 100 series (P or R) filters Using a chipper in a small unventilated area None Full enclosure systems (with negative air) are required to restrict access to and contain the work area Full-face powered air-purifying respirator (PAPR) with 100 series (P or R) filters Jackhammering a small area of floor LEV (could include a sleeve on the tool, connected to a HEPA vacuum or negative air unit) Barriers (for example, a tape barrier) to restrict access to the work area Half-face respirator with 100 series (N, P, or R) filters Continuous water spray (could include a portable airless sprayer, air mister, or hose sprayer) Barriers (for example, a tape barrier) to restrict access to the work area Half-face respirator with 100 series (N, P, or R) filters Jackhammering a large area of floor (or using more than one tool in an area) LEV (could include a sleeve on the tool, connected to a HEPA vacuum or negative air unit) Barriers (for example, a tape barrier) to restrict access to the work area Full-face respirator with 100 series (P or R) filters Continuous water spray (could include a portable airless sprayer, air mister, or hose sprayer) Barriers (for example, a tape barrier) to restrict access to the work area Full-face respirator with 100 series (P or R) filters Using a jackhammer in a small unventilated area None Full enclosure systems (with negative air) are required to restrict access to and contain the work area Full-face powered air-purifying respirator (PAPR) with 100 series (P or R) filters Safe work planning Select one or more of the methods described in the table above. Establish a barrier or full enclosure (under negative pressure) around the work zone to restrict access by unprotected workers. Inspect all dust control equipment and tools to make sure they are in good working order. Use and maintain all tools and equipment as specified by the manufacturer. For example, test the effectiveness of HEPA filters using dioctyl phthalate (DOP) testing or similar means at least annually, and any time a HEPA filter is replaced in a vacuum cleaner or ventilation system. When working on a multi-employer site, provide the general contractor with a copy of the silica exposure control plan and safe work procedures. Review the procedures and work schedule with the general contractor to determine if additional measures are required to reduce worker exposure to silica. Ensure that workers inspect their respirators before start-up. Visually monitor dust release from equipment during use. When tools and equipment are working properly, very little dust should be visible in the air. Stop work if excessive dust is observed. Respiratory protective equipment Each worker will be fit tested if a respirator is required. If a worker is required to wear a respirator that requires an effective seal with the face for proper functioning, the worker must be clean shaven where the respirator seals with the face. When the worker notices a notable resistance to breathing, the respirator filters must be replaced. Respirators will be used, cleaned, and stored in accordance with the respiratory protection program. Other personal protective equipment and hygiene Workers will wear approved safety goggles and hearing protection when chipping or jackhammering concrete. This equipment will not interfere with the fit of the worker’s respirator. Workers will wear washable work coveralls that do not retain dust. These coveralls will be laundered and changed regularly, and workers will not wear them outside the work area. For example, workers must remove coveralls before eating lunch. Workers who launder clothing contaminated with silica should be informed of the hazards of silica and the precautions required for handling the clothing. Disposable coveralls will be used in full enclosure systems. Housekeeping procedures Dry sweeping and the use of compressed air are prohibited for removing dust and debris containing silica. Work areas and equipment covered by dust will be cleaned at the end of every shift using a HEPA filter vacuum. Wet cleanup may also be used to remove dust. Any slurry generated by wet control methods should be cleaned up when the work is completed to avoid secondary dust exposure hazard. Waste material will be placed in a dumpster, and will be removed at least weekly. The location and method used to store waste will not allow silica-containing dust to re-enter the workplace. Supervisors are responsible for ensuring that work areas are free from dust at the end of each shift. Worker training for silica dust exposure Training will be performed by the employer or the employer’s designate. Records of attendance, dates of training, and training material will be documented and retained. Additional training or reference material on silica dust exposure will be made available to employees upon request. Training topics Health hazards of silica dust exposure (including signs and symptoms of silicosis) Operations and materials that can produce silica dust exposures Engineering controls and safe work practices used to protect workers The importance of proper equipment control and maintenance Housekeeping procedures Proper use of respirators and the respirator program Personal hygiene procedures to reduce exposures How smoking increases the risk of developing silicosis and other lung damage The details of the exposure control program for silica dust Health surveillance Workers who are regularly exposed to silica dust will receive regular medical examinations from their family physicians. These examinations may include chest X-rays. Workers will report any symptoms of silica exposure to the employer and WorkSafeBC for tracking and investigation. Annual review This ECP will be reviewed at least annually and updated as necessary by the employer, in consultation with the workplace health and safety committee or the worker health and safety representative. |
| --- | --- | --- |