Exposure control plan for cutting, grinding, and polishing stone containing crystalline silica (quartz)

The cutting, grinding, and polishing of stone (e.g., granite) without proper dust controls can generate high levels of silica-containing dust. Breathing in this fine dust can cause a serious lung disease called silicosis, which is characterized by scarring and thickening of the lungs, and can result in death.

|  |  | Protecting workers when cutting, grinding, and polishing silica-containing stone |
| --- | --- | --- |

| This document will help employers develop an exposure control plan (ECP) for work involving the cutting, grinding, and polishing of stone containing crystalline silica. An ECP is a requirement of the Occupational Health and Safety Regulation (the Regulation). The ECP sets out a detailed approach to protecting workers from harmful exposure to crystalline silica dust. Employers can use this document as a template and add specific details regarding safe work practices in their operations. This document covers the points employers need to follow to protect workers from harmful exposure. It is important to follow all the points or use equally effective measures. Tools and equipment for cutting, grinding, and polishing stone Grinders Stationary grinders work well for larger jobs. Hand-held portable grinders are also used. Circular saws A number of equipment manufacturers make saws designed for cutting stone slabs. These saws are equipped with water attachments for wet-cutting using diamond blades. Vacuums Both dry and wet vacs may used. These need to be fitted with HEPA filtration to prevent respirable silica from entering the workplace air. Equipment tips Invest in good quality equipment and keep it well maintained. Well-designed and maintained equipment significantly reduces dust and lasts longer between replacement and maintenance. A variety of specially designed equipment is available for cutting stone. Respirator program Employers whose workers wear respirators are required to develop and implement a respirator protection program. The WorkSafeBC publication Breathe Safer provides guidance for developing this program. Hearing conservation Workers in stone shops are exposed to high levels of noise. Over time, workers exposed to these noise levels will suffer hearing loss. Noise hazard signage must be posted in these areas. Workers must wear appropriate hearing protection in these areas. Additional information The following WorkSafeBC publications are available from WorkSafeBC.com: Breathe Safer (click Publications) Toolbox Meeting Guides for Hazardous Materials: Silica (click Safety at Work, then in the Quick Links section click Toolbox Meeting Guides, and then click Hazardous Materials) For more information about health and safety, employers and workers can call the WorkSafeBC Prevention Information Line and ask to speak with an occupational hygiene officer. Call 604 276-3100 in the Lower Mainland or 1 888 621-7233 toll-free in B.C. Useful links HSE leaflets on silica and construction can be downloaded free from the HSE web site at www.hse.gov.uk/pubns. NIOSH publications are available at no charge at www.cdc.gov/niosh (search silica and construction). |  | Company information Name Address Contact information (names and phone numbers) Worksite information Project name Address Health hazards from silica exposure Long-term exposure to airborne crystalline silica (e.g., quartz) can cause a disabling, sometimes fatal lung disease called silicosis. When the dust is inhaled deep into the lungs, microscopic particles of silica can cause scar tissue to form in the lung tissue, which restricts the lungs’ ability to extract oxygen from the air. This damage is permanent, but symptoms of the disease may not appear for many years. The disease initially causes fatigue and shortness of breath. If exposure continues, it can lead to chest pain, heart problems (difficulty breathing can strain the heart), and respiratory failure. Exposure to crystalline silica has also been liked to other diseases, including bronchitis, tuberculosis and lung cancer. Purpose and responsibilities We have a duty to protect our workers from silica exposure during the manufacture of our stone products. Studies show that work tasks involving the cutting, grinding, and polishing of silica-containing stone products generate airborne silica levels well in excess of safe levels. Effective controls are available to protect workers from harmful exposure. We know that a combination of control measures will be required to achieve this objective. We commit to being diligent in our efforts to select the most effective control technologies available, and to ensure that the best practices, as described in this exposure control plan (ECP), are followed at our worksites. The work procedures we establish for cutting, grinding, and polishing silica-containing stone will protect not only our workers but also any other workers on-site who are not involved in these operations. The employer is responsible for the following: Ensure that the materials (i.e., tools, equipment, and personal protective equipment [PPE]) and other resources (i.e., worker training) required to fully implement and maintain this ECP are readily available where and when they are required. Ensure that all required tools, equipment, and PPE are readily available and used as required by the ECP. Ensure that supervisors and workers are educated and trained to an acceptable level of competency. Maintain records of training, fit-test results, crew talks, and inspections (for equipment, PPE, and work methods and practices). Conduct a periodic review of the effectiveness of the ECP. This includes a review of available dust control technologies to ensure these are selected and used when practical. Coordinate the work with the prime contractor and other employers to ensure a safe work environment. Supervisors are responsible for the following: Provide adequate instruction to workers on the hazards associated with the cutting, grinding, and polishing of silica-containing stone. Select and implement the appropriate control measures. Ensure that workers using respirators have been properly fit-tested and that the results are recorded. Direct the work in a manner that ensures the risk to workers and others is minimized and adequately controlled. This includes ensuring that workers use appropriate engineering controls and wear the necessary PPE. Workers are responsible for the following: Use the assigned protective equipment in an effective and safe manner. Follow established work procedures as directed by the supervisor. Report any unsafe conditions or acts to the supervisor. Report any exposure incidents or any signs or symptoms of silica illness. Risk identification and assessment Stone (e.g., granite) can contain a high percentage of silica. Cutting, grinding, and polishing stone without the use of proper dust controls and PPE can expose workers to levels of airborne respirable crystalline silica that are above the exposure limit listed in the Occupational Health and Safety Regulation. Work locations where workers or other persons are exposed to the hazards of silica will be identified with signs, placards, or barrier tape. Exposure limit The occupational exposure limit (OEL) for respirable crystalline silica (including quartz) is 0.025 milligrams per cubic metre (mg/m3). Because crystalline silica is linked to lung cancer, workplace exposures must be reduced to levels that are as low as reasonably achievable (ALARA) below the OEL. Silica dust control The Regulation requires employers to select silica dust controls based on the following hierarchy: Engineering Administrative controls Personal protective equipment (PPE) Use of respirators as a primary control is not acceptable when other methods are available and practical. Respirators will be used in conjunction with other controls such as wet cutting, grinding, and polishing to reduce worker exposure to silica, unless air monitoring information suggests otherwise. Wet cutting, grinding, and polishing or the use of local exhaust ventilation (LEV) are the preferred engineering methods and will be used when practicable. Dry cutting, grinding, and polishing will be avoided unless additional respiratory protection and other controls are used. Dry cutting or grinding methods might be required for certain applications or work locations. Dry work will be isolated from other work areas. Effective LEV will be used in order to control the dust. A HEPA vacuum will be used for cleanup and decontamination. Air discharged from an LEV system will not be recirculated into the work area. Acceptable control methods for cutting, grinding, and polishing stone The work methods in the following table are acceptable, provided that the respirator selection is adhered to. The following control options will be used to eliminate or reduce the risk to workers from the hazards of silica dust exposure, unless air monitoring information suggests otherwise: Cutting, grinding, and polishing method/tools Dust suppression Work location Respirator type Circular saw on table Water Stone shop N95 respirator Hand-held circular saw Water Stone shop Half-face respirator with N100 filters Hand-held polisher Water Stone shop Half-face respirator with N100 filters Circular saw (less than one hour per shift) HEPA vacuum extraction On-site installation Half-face respirator with N100 filters Circular saw (more than one hour per shift) HEPA vacuum extraction On-site installation Full-face respirator with N100 filters Circular saw None* Stone shop Full-face (PAPR) respirator with N100 filters * This work should be conducted in isolation from the general shop and other workers, with some form of general exhaust ventilation. Safe work planning Select one or more of the methods described in the table above. Establish a barrier around the work zone to restrict access by unprotected workers. Inspect all dust control equipment and tools to make sure they are in good working order. Use and maintain all tools as specified by the manufacturer. When working off-site, provide the general contractor with a copy of the silica exposure control plan and safe work procedures. Ensure that workers inspect their respirators before start-up. Monitor dust release from equipment during use. When tools and equipment are working properly, very little dust should be visible in the air. Stop work if excessive dust is observed. Respiratory protective equipment Each worker will be fit-tested if a respirator is required. When the worker notices a notable resistance to breathing, the respirator filters must be replaced. Respirators will be used, cleaned, and stored in accordance with the respiratory protection program. Other personal protective equipment and hygiene Workers will wear approved safety glasses and hearing protection when cutting silica-containing stone. This equipment will not interfere with the fit of the worker’s respirator. Workers will wear washable work coveralls that do not retain dust. These coveralls will be laundered and changed regularly, and workers will not wear them outside the work area. Housekeeping procedures Dry sweeping and the use of compressed air are prohibited for removing dust and debris containing silica. Work areas and equipment covered by dust will be cleaned at the end of every shift using a HEPA filter vacuum. Wet cleanup may also be used to remove dust. Waste material will be placed in a dumpster and will be removed at least weekly. The location and method used to store waste will not allow silica-containing dust to re-enter the workplace. Supervisors are responsible for ensuring that work areas are free from dust at the end of each shift. Worker training for silica dust exposure Training will be performed by the employer or the employer’s designate. Records of attendance, dates of training, and training material will be documented and retained at the stone shop. Additional training or reference material on silica dust exposure will be made available to employees upon request. Training topics Health hazards of silica dust exposure (including signs and symptoms of silicosis) Operations and materials that can produce silica dust exposures Engineering controls and safe work practices used to protect workers The importance of proper equipment control and maintenance Housekeeping procedures Proper use of respirators and the respirator program Personal hygiene procedures to reduce exposures How smoking increases the risk of developing silicosis and other lung damage The details of the exposure control program for silica dust Health surveillance Workers who are regularly exposed to silica dust will receive regular medical examinations from their family physicians. These examinations may include chest x-rays. Workers will report any symptoms of silica exposure to the employer and WorkSafeBC, for tracking and investigation. Annual review This ECP will be reviewed at least annually and updated as necessary by the employer, in consultation with the workplace health and safety committee or the worker health and safety representative. |
| --- | --- | --- |