SAFEWORK PROCEDURE – WORKING ON ROOF OF CITY HALL BUILDING

Background:

The following procedures have been developed for working on these roofs:

- Procedure For Building roof- control zone

  - The roof is level.

  - Roof access is gained by a ladder located in the centre of the roof through a hatch.

  - Most work cleaning drains, servicing air handling units and work in the boiler room 	shall be inside the painted line (outside the “control zone” in the “safe zone”).

  - When work is required inside the control zone where there is not a guardrail, 	workers must either use fall restraint (harness, lanyard, vertical lifeline and rope 	grab anchored and positioned to keep the worker from reaching the edge) or the 	control zone/safety monitor whereby an additional worker must be present in the 	“safe zone” with a high visibility vest and monitor the worker’s activity inside the 	control zone.  The control zone boundary will be demarked/raised with stanchions 	and tape/rope when this method is used.

- Procedure For Light duty, short duration work

  - The roof is level.

  - Be aware of weather conditions

3.3	Plan your job ahead of time to minimize length of time for work near the roof edge.  	Generally there is minimal work and time spent on the roof (cleaning roof drains, 	inspecting)

  - Approach the roof edge from the center of the roof.

  - Worker to keep their center of gravity as far back as possible from the roof edge.

  - Do not turn your back to the roof edge when approaching or retreating.