| Department: | Public Works |  |
| --- | --- | --- |
| Subject: | #417 Flushing – Safework Procedure |  |

#417 - FLUSHING

Purpose:

The City of Nanaimo maintains the wastewater collection system through the safe operation of Unit #417.  This combination flusher\hydro vac truck is a mobile unit which responds to a variety of tasks within the City including emergency repairs to City infrastructure.

HAZARDS:

| Moving parts | Contamination from biohazards | High pressure water |
| --- | --- | --- |
| Flying debris | Working in or around excavations and confined spaces | Working around traffic and mobile equipment |

PPE:

| Hardhat (when required) | PVC gloves | Hi Vis vest or coveralls |
| --- | --- | --- |
| Eye protection | Safety boots | Hearing protection (when required) |

**Tetanus and Hepatitis shots recommended.

Pre-Setup:

- Set up safe work zone.

- Use traffic control when required.

- Park truck to allow safe and easy operation of hose reels.

Procedure:

- Engage truck into pump mode.  **Ensure truck is in fourth gear before stepping out of vehicle.

- Safely remove manhole cover and assess entry into channel for flushing hose and nozzle.

- Position and lock hose reel accordingly and lower tigertail, hose and nozzle into channel using hose reel controls on front control panel.

- With truck at idle, charge rodder using pressure control dial on control panel.

- Advance hose through pipe at desired pressure to destination.  Co-worker can advise with use of hand signals or radio.

- Slowly retrieve rodder through pipe back to manhole or pipe opening.

- When black leader hose is visible, rodder is almost back to start.  Release hose control lever and turn pressure dial to off position.

Flushing Open-Ended Pipe And Culverts:

- Ensure co-worker is positioned at upstream end of pipe to prevent rodder from coming out of pipe.

- Feed out enough hose slack to allow operators to manually insert nozzle into pipe opening if required.

Post Setup:

- Ensure rodder is turned off at end of flushing run.

- Retrieve rodding hose out of pipe or manhole using hose reel controls, replace manhole cover.

- Wrap hose on reel while retrieving hose.

- Stow away nozzle and skid at bottom of hose reel.  Engage truck back to road mode.

- Tear down safe work zone.

Summary:

- It is important to always be aware that hands, hair, loose clothing can get caught in hose reel while moving.

- Eye protection shall be work at all times.

- Requires two fully trained operators at all times.

- Be aware of operating pressure at all times.

- Nozzle may be under high pressure and could cause extreme damage or harm if it escapes from pipe.

- Always have one person at control panel to shut down in case of emergency.

- Be aware of flying debris.

- Ensure debris hopper door is closed before starting shift.

- Ensure debris hopper is cleaned and door is open at end of each shift.

- Be aware of “pinch points”

- Most levers, handles, and tools on #417 may be contaminated. Never open door handles with gloves on and always wash hands before eating.

- When flushing, it is advisable to wear a particulate mask when mists from sewer manholes are extreme.

| Date: 2010-Mar-30 Revision Date | Written by: Riley St. Luke Manager’s Approval: John Elliot |
| --- | --- |

g:\adminstration\reference material\unit 417 flushing.doc