| Department: | Public Works |  |
| --- | --- | --- |
| Subject: | #417 Hydro-excavating – Safework Procedure |  |

#417 – HYDRO-EXCAVATING

PURPOSE:

With the use of Unit #417 hydro-excavating capabilities, the City of Nanaimo can respond to a variety of emergency repairs to infrastructure using a combination of high pressure water and vacuum.  Unit #417 can safely excavate and expose other utilities that may be difficult or hazardous with conventional equipment.

HAZARDS:

| Contamination from biohazards | Working near overhead hazards |
| --- | --- |
| High noise levels | Working around traffic and mobile equipment. |
| Flying debris | High pressure water and vacuum |
| Working around gas, hydro and other underground utilities | Working in or around excavations and confined spaces |

PPE:

| Hardhat | Hi Vis Vest or coveralls | Hearing protection |
| --- | --- | --- |
| Gloves | Eye protection | Safety boots |

**Tetanus and Hepatitis shots recommended.

Pre-Setup:

- Set up safe work zone.

- Be sure pre-ex is on site for review

- Use traffic control when required.

- Park truck to allow safe and easy operation of hydro-excavating procedures.

Procedure:

- Engage truck into pump mode then blower mode.  **Ensure truck is in fourth gear before stepping out of vehicle. Engage hydro-excavating switch in cab.

- Tube setup – requires two people:

- Check for overhead hazards before setting up tubes.

- Ensure vacuum relief valve is open

- Using boom controls, elevate rubber hose on end of boom high enough to insert spigot end of aluminum tube into bell on rubber hose.

- Lower to ground level then apply clamp.

- Repeat if more tubes are needed.

- Boom operator to keep one hand on tubes while excavating or moving boom whenever possible.

- When using 4” tube, close vacuum relief and insert bell end of tube on to bell end of rubber hose.

- Tube is held in place by vacuum.

- To release tube, open relief valve while holding onto 4” tube.

- Digging wand:

- Pull out sufficient length of hose from hose reel for digging wand.

- Attach hose to digging wand

- Charge wand at tool circuit

- Hydro-excavating:

- This procedure requires two fully trained operators – one to control boom and one to control digging wand.

- Be sure work area is clear of bystanders and hopper door at back is closed.

- Position digging tube over area to be excavated approximately 6 inches above ground.

- Vacuum relief valve is in closed position.

- Adjust throttle control until 1300 – 1500 PRM is reached.

- Aim wand nozzle directly under digging tube and depress trigger.

- Lower digging tube as it sucks up material loosened by digging wand to achieve desired size of excavation.

Post Setup:

- Turn throttle to off position at control panel

- Return tool circuit to neutral position

- Depress trigger on wand to relieve pressure

- Remove wand from hose and put both away

- Reverse steps for tube set-up and put away

- Engage truck back to road mode

- Shut off hydro-excavation toggle in cab

- Tear down safe work zone

Summary:

- It is important to remember that high water pressure and high levels of vacuum are present at all times while hydro-excavating.  Do not attempt to unclog digging tube unless vacuum relief valve is open and boom operator gives the okay.  Engine is at idle.

- Never point digging wand at anyone.

- Only reach into a hole when the vacuum relief valve is open.  The digging wand is pointed away from hole and boom operator gives the okay.

- Keep hands, loose clothing, etc. away from vacuum end of tubes at all times.

- Open relief valve in case of emergency.

- Ensure debris hopper door is closed before starting shift.

- Ensure debris hopper is cleaned and door is open at end of shift

- Be aware of “pinch points”

- Safely insert “ground pin” when working around gas or hydro

- Most levers, handles, and tools on #417 may be contaminated. Never open door handles with gloves on and always wash hands before eating.

| Date: 2010-Mar-30 Revision Date | Written by: Riley St. Luke Manager’s Approval: John Elliot |
| --- | --- |

g:\adminstration\safety\oh&s subcommittee pw\safework procedures\unit 417 hydro-excavating.doc