| Department: | City of Nanaimo |  |
| --- | --- | --- |
| Subject: | Small Roof Access Safe Work Procedure |  |

Small Roof Safe Work Procedure

(< 40 feet wide)

Note: City workers do not access higher sloped roofs (> 4 vertical by 12 horizontal)

Ladder Use: (Use ladder as much as possible)

- Two person job

- Set up ladder away from corners

- Ensure four point ladder contact (two feet, two rails)

- Have second person hold ladder to prevent its movement

- Climb and perform light work <15 min using at least 3 point contact (two feet and one hand)

- Keep center of gravity between rails

Accessing Roof Top:

- Set up ladder at least 3 rungs above roof edge

- Have second person hold ladder while climbing onto roof

- Climb one rung above roof edge and carefully step onto roof and face ladder holding onto rails so partner can climb ladder

- Immediately move to the center of roof to continue to plan work

Control Zone Procedure: (entire roof is declared as the control zone)

Safety monitor to remain in safe location (usually in center of roof) and:

- Be experienced in the work overseen and trained in the role of safety monitor

- Be present at all times when a worker is in the control zone

- Have complete authority over the work as it relates to the prevention of falls

- Engage in no other duties while acting as the safety monitor

- Be located so as to have a clear and continuous view of the work

- Be able to have normal voice communication with the workers being protected

- Monitor no more than 8 workers

- Be instantly distinguishable from other workers

Worker to:

- To approach roof edges (control zone) directly from center of roof

- Do not move along roof edge

- Minimize time at roof edge

- Keep center of gravity low

- Always face the roof edge, even when moving back towards roof center

| Date: 2010-Jan-04 Revised: | Author: B. Browett, J. Dunn Approved by: Rick Kroeker |
| --- | --- |