Written Safe Work Procedure for Cleaning Up Asbestos-Contaminated Drywall in Volumes Equal To or Less Than 1 Cubic Meter

DATE CREATED: November 15, 2011		LAST REVISION DATE:

TOOLS AND EQUIPMENT REQUIRED:

- Traffic Control Equipment

- High Visibility Vests

- Disposable Tyvek Coveralls (hooded with elastic wrists and ankles)

- NIOSH-Approved Half-Face or Full-Face Respirator w/ P-100 Filters

- NIOSH-Approved Protective Gloves

- NIOSH-Approved Protective Eye Wear (if using Half-Face respirator)

- NIOSH-Approved Protective Foot Wear (Seamless Rubber Boots)

- Two Wash Buckets for each two employees

- Hand Soap

- First Aid Kit

- Duct Tape

- Pylons/Sawhorses/Traffic Cones

- Asbestos Warning Tape

- Minimum of 4 Asbestos Hazard Signs

- Asbestos Waste Bags

- Disposable Hand Towels

- 6 Mil Polyethylene Sheeting

- Spray Canister Capable of Misting

- Shovel/Hand Spade

PROCEDURE

- Ensure traffic control is in place in accordance with the British Columbia Ministry of Transportation and Highways Traffic Control Manual and Municipal – specific procedures.

- Cordon off the work area using a combination of asbestos warning signs, pylons/ traffic cones/sawhorses, and asbestos barrier tape to restrict access to the work area by unauthorized personnel.  Ensure asbestos warning signs are placed around the work area.

- The barricaded asbestos work area will be constructed with a personal decontamination area immediately adjacent, limiting access to and from the asbestos work area.

- Place 6 mil polyethylene sheeting drop sheets on the ground within the personal decontamination area and immediately adjacent to the asbestos clean-up area.

- Place the following items on the drop sheets, within reach of workers inside the asbestos clean-up area:

  - Two wash buckets for every two employees, filled with water

  - Hand soap

  - Disposable Hand Towels

  - Asbestos Waste Bags

  - Duct Tape

- Don Personal Protective Equipment before entering asbestos clean-up area:

  - Disposable Tyvek Coveralls with hood, and elastic at wrists and ankles

  - High Visibility Vests

  - NIOSH Approved Half-Face or Full-Face Respirator w/ P-100 Filters

    - Perform positive and negative pressure fit check

  - NIOSH Approved Protective Gloves

  - NIOSH Approved Protective Eye Wear (if using Half-Face respirator)

  - NIOSH Approved Protective Foot Wear (Seamless Rubber Boots)

  - Hearing Protection (if required)

  - Hard Hat (if required)

    - Duct tape around wrists and cuffs of coveralls.

- Every worker inside the asbestos clean-up area shall wear personal protective equipment at all times and follow the appropriate personal decontamination procedure when exiting the asbestos clean-up area.

- Before starting any work that is likely to disturb the asbestos-containing drywall, mist water onto the waste.  During the work, continuously mist water onto the waste pile that is being cleaned up.

- Clean up dust and waste by shovel or hand.

- Double-bag the waste into asbestos waste bags over the 6 mil polyethylene sheeting drop sheet, as follows:

  - gently squeeze the bag to expel air

  - Tightly twist the unused top portion of the bag into a tail and seal with duct tape at the base of the tail.

  - Take the leftover tail section of the bag and bend it around to make a loop and attach it to the base of the tail using the duct tape.

  - Place the first bag into the second bag and place on drop sheet.

- Visually inspect the barricaded work area thoroughly to ensure all asbestos-containing material and dust/debris has been fully removed.

- Immediately upon finishing the work, complete the following tasks:

  - Rinse tools in bucket of water, inspect; wipe with wet cloth if necessary.  Rinse in second bucket, set aside;

  - Damp wipe disposable coveralls; remove and place in asbestos disposal bag;

  - Exit the asbestos clean-up area;

  - Wet drop sheet;

  - Place barrier tape on drop sheet.  Fold drop sheet to contain any remaining dust;

  - Place into an asbestos waste bag;

  - Double bag the waste into a second asbestos waste bag and set aside as noted in #10 above;

  - Clean the outside of the respirator and remove;

  - Thoroughly wash hands and face;

  - Wash and rinse the inside of the respirator;

  - Tape over the respirator filters or dispose of as asbestos waste.

  - Dump the clean-up water in a storm drain.  Wipe out the bucket and dispose of rags as asbestos waste.

- Transport asbestos waste as a hazardous waste and in accordance with the requirements of the Transportation of Dangerous Goods Act and Regulations.

Personnel Exiting the Work Area (Personal Decontamination)

This process is to be followed by every worker each time they leave the asbestos clean-up area.

      - One entrance and exit will be used and maintained by all workers.

      - Each time the worker leaves the work area he/she will damp wipe his/her disposable coveralls to remove visible debris, within the work area.

      - Still within the work area, the worker will remove coveralls and place in a 6 mil asbestos-waste-labelled polyethylene bag and dispose of as asbestos waste. DO NOT REMOVE RESPIRATOR AT THIS TIME.

      - Still wearing the respirator, the worker will proceed to a designated “personal decontamination” area provided.

      - In the personal decontamination area, thoroughly clean the outside of the respirator with water.

      - Remove the respirator.

      - Thoroughly wash hands and face.

      - Wash and rinse the inside of the respirator.

      - Respirator filters will be taped over while respirator is not in use to prevent possible release of entrapped asbestos fibres.

      - If this is the last use of the filter cartridges, they must be disposed of as asbestos waste

      - Exit the “clean area”.

Tool Decontamination

Tools and materials must be thoroughly rinsed in a bucket of water and inspected (to ensure there is no asbestos contamination) before being removed from the authorized work zone.   Any remaining pieces of debris shall be wiped off using a damp cloth.   Following this clean up, tools must be rinsed in the second bucket of clean water and placed outside the asbestos clean-up area.

If the object is too large to be washed in a bucket of water, such as a shovel, use a wet cloth to wipe the object down until visually clean.  Inspect thoroughly for asbestos contamination and repeat if necessary until all material has been removed from the item.